## Slide 1
Spatially constrained Bayesian inversion of frequency-
and time-domain Airborne ElectroMagnetic data from the Tellus project
Duygu Kiyan1, Volker Rath1, and Robert Delhaye1
1School of Cosmic Physics, Geophysics Section, Dublin Institute for Advanced Studies, Dublin, Ireland
28 April, 2017

## Slide 2
The airborne geophysical survey comprises measurements of magnetic field, radiometrics and electrical conductivity of the near-surface.
The data will inform the management of
Ireland’s natural and environment resources.
The data are used to:
update and improve geological maps
improve radon risk mapping
map groundwater systems, e.g., identifying
groundwater pathways in the subsurface
Tellus Project – Airborne Geophysics Component
Figure courtesy: Geological Survey of Ireland
AEMPY is a python toolbox developed for inversion of frequency- and time-domain airborne electromagnetic data of the TELLUS Surveys.

## Slide 3
Conversion to Internal Data Format
FDEM Format
XUTM, YUTM, GPS, RADAR, IP912-24510, Q912-24510, PWLM
TDEM Format
XUTM, YUTM, GPS, RADAR, X1-X11, Z1-Z11
Define Dataset
Flight-line, polygon, profile projection
Pre-Processing
- Flag negative values and high-fly areas
- Interpolate
- Average/Block Data over a Number of
Stations
- PCA filtering
Inversion Along Flight Line
Deterministic Approach
Tikhonov-type inversion
MAP inversion
Truncated SVD Inversion
Stochastic Approach
Markov Chain Monte Carlo
AEMPY Workflow
Input File
Tellus
FDEM & TDEM Data

## Slide 4
Spatially constrained Bayesian inversion of frequency-
and time-domain Airborne ElectroMagnetic data from the Tellus project
Duygu Kiyan1, Volker Rath1, and Robert Delhaye1
1School of Cosmic Physics, Geophysics Section, Dublin Institute for Advanced Studies, Dublin, Ireland
28 April, 2017

## Slide 5
The Tellus Project – Airborne Geophysics Component
Figure courtesy: Geological Survey of Ireland
AEMPY is a python toolbox developed for inversion of frequency- and time-domain airborne electromagnetic data of the TELLUS Surveys.
The airborne geophysical survey comprises of measurements of magnetic field, radiometrics and electrical conductivity of the near-surface.
The data will inform the management of
Ireland’s natural and environment resources.
The data are used to:
update and improve geological maps
improve radon risk mapping
map groundwater systems, e.g., identifying
groundwater pathways in the subsurface

## Slide 6
Python & Fortran90
CSIRO/Amira forward codes
Modules and Scripts
Numpy, Scipy, Matplotlib
DIAS GIT Repository
Free Access
AEMPY is a python toolbox developed for inversion of frequency- and time-domain airborne electromagnetic data of the TELLUS Surveys
IMPLEMENTATION
What is AEMPY?

## Slide 7
Conversion to Internal Data Format
FDEM Format
XUTM, YUTM, GPS, RADAR, IP912-24510, Q912-24510, PWLM
TDEM Format
XUTM, YUTM, GPS, RADAR, X1-X11, Z1-Z11
Define Dataset
Flight-line, polygon, profile projection
Pre-Processing
- Flag negative values and high-fly areas
- Interpolate
- Average/Block Data over a Number of
Stations
- PCA filtering
Inversion Along Flight Line
Deterministic Approach
Tikhonov-type inversion
MAP inversion
Truncated SVD Inversion
Stochastic Approach
Markov Chain Monte Carlo
AEMPY Workflow
Input File
Tellus FDEM & TDEM Data

## Slide 8
Tellus Project Airborne EM systems
Frequency-Domain AEM:
Instrument: JAC Airborne System - AEM05
Aircraft: De Havilland DHC-6 twin Otter (C-GSGF)
Flight Line spacing: 200m
Tie Line spacing: 2000m
Nominal Flight height: 59m (in rural areas)
240m (in urban areas)
Time-Domain AEM:
Instrument: TEM-GENESIS System
Aircraft: Cessna 208B (VH-ZKG and VH-ZKB)
Flight Line spacing: 200m
Tie Line spacing: 2000m
Nominal Flight height: 90m (in rural areas)
240m (in urban areas)

## Slide 9
Data Visualisation
Scatter Plots
Interpolation Plots

## Slide 10
Along Flight-Lines
Plots
Data Visualisation
Notes: Fumarole area – 200m depth 200 degrees.

## Slide 11: Data Pre-Processing
PCA Analysis:
Remove High Fly data points: e.g., radar data > 70 m
Flight Line: 1379

## Slide 12
Field Data – Tellus A1 Block
(from Blake et al., 2016)
Maps of Apparent Resistivity Data derived from
Tellus A1 Block AEM Data

## Slide 13
(after, Blake et al., 2016)
3-D High-Frequency Magnetotelluric Data

## Slide 14: Data Inversion – Along Flight Lines
Tikhonov-type inversion results using raw data and blocked data of Tellus Block A1 Survey:
Block Data: data were summarised by their per-frequency arithmetic mean over 10 stations.
Inversion Parameters:
100 ohm-m randomly perturbed half-space model, 40 layers, with approx. 4m thick, fixed during the inversion

## Slide 15: Bayesian MCMC – Synthetic Data
Time-Domain AEM Results
Starting Model: 100 ohm-m, randomly perturbed
Number of layers: 12, approx. 5m thick, fixed
Assumed Data Error: 0.01
Number of samples: 100,000
Simulation Parameters Set-up:
100ohm-m
5ohm-m
100 ohm-m
15m
25m
True Model:
A summary of the output from the Metropolis-Hastings algorithm

## Slide 16: Bayesian MCMC – Synthetic Data
100ohm-m
5ohm-m
100 ohm-m
15m
25m
True Model:
Frequency-Domain AEM Results
Starting Model: 100 ohm-m, randomly perturbed
Number of layers: 3, approx. 40m thick, not fixed
Assumed Data Error: 30 ppm
Number of samples: 1,000,000
Simulation Parameters Set-up:
A summary of the output from the Metropolis-Hastings algorithm

## Slide 17: Summary/Conclusions
State of the toolbox:
Free Python framework exists for processing and inversion of airborne time- and frequency –domain airborne EM
Numerous algorithms are implemented
  Processing: imputation/interpolation of gaps, PCA analysis
  Inversion: Tikhonov and MAP deterministic inversions, MCMC
On-going and Future Work:
Fill public repository with tested scripts
Case studies for real world data
Better error model
More systems (legacy GEOTEM data)
More algorithms for inversion
  Deterministic (Sharp boundaries, image guided)
  Stochastic (trans-dimensional, hybridisation)
From 1-D to 2(3)-D models
Work flows for large data sets (parallelism), in particular MCMC

## Slide 18
Acknowledgements
DK was funded by the Geological Survey of Ireland (GSI) under the research grant sc2015-004. We would like to thank the GSI team, especially James A. Hodgson and Mohammednur Dessisa Ture, who were most helpful and co-operative, and thus contributed considerably to this work. Australia’s CSIRO and the AMIRA International consortium are thanked for making their P223 modelling suite open access.

## Slide 19: References
Blake et al., 2016. Electromagnetic imaging of hydrothermal circulation systems beneath two
thermal springs in Ireland, presented at IRETHERM Workshop, April 1, 2016, Dublin, Ireland.
Hodgson, J.A. and Ture M.D., 2016. Tellus A1 Airborne Geophysical Survey Logistics, Processing
and Merging Report.
Lanczos, C., 1961. Linear differential Operators. D. Van Nostrand Co. Ltd.

## Slide 20: PCA Denoising Analysis:
Decomposition in principal components (PCA) is to reduce noise and impose regularity (consistence) on the data.
PCA approximation is based on the singular value decomposition (SVD, Lanczos, 1961).
 ndata  nsites Matrix of an observation, D, remove average and standardize
 decompose: (U , V unitary, S diagonal, singular values)
 choose k largest values and truncate to
 Independent estimate of error (high-fly) indicate that k> 3 is probably “noise”
27/30 ppm
44/27 ppm
43/25 ppm
57/41 ppm

## Slide 21: PCA Denoising Analysis
Why k ≤ 3?
Error limit from the high-fly areas
Error limit from the high-fly areas

## Slide 22: “Deterministic” inversion
Examples
Tikhonov-type regularization (stabilize ill-posed problem)
MAP estimates derived from Bayesian theory
Produces only one optimal model, may be biased by choice of data fit and model constraints (smoothness, blockyness)
Fast, but usually needs derivatives (“Jacobian”, “sensitivity”)
Many variants (as Tikh and MAP) may be solved within the same computational framework
Optimization problem: